Feature                            Electric Durasweeper                       Units

Unit height

Unit width

Unit inner width

6293                                              mm

9508                                              mm

3741                                              mm

Unit length

3784                                              mm

Frame weight

1554                                              kg

Total weight

2200                                              kg

Input power

Max. working height Min. working height Max. truck width

400 V, three-phase, 50 Hz

5405

416

3000

V, Hz mm mm

mm

Brush segment diameter

800                                                mm

Brush material

Brush segment length

Polypropylene (blue)

1200 (x3)

N/A

mm

Brush segment weight

40 (x3)                                           kg

Average snow removal time

Recommended vehicle speed

0.45 (for 13.6 m truck length)

3

min

km/h

Unit structure

Stainless Steel 1.4301 (AISI 304) N/A

Structure finish

Powder Coat

N/A

Concrete pad

Hardware

See provided foundation plan

Assembly Hardware and Wedge

Anchors Provided		   
N/A

Levering dispersion sound pressure scale in working place

71.5

dB

Maximum brush working height (max truck height) - 5405 mm.

Maximum truck 5405 mm

416 mm

width – 3000mm.

Minimum brush working height -416 mm.